## Slide 1: Video Communications on the Go
Norman Williams
Senior Research Engineer
Technology Access Program
Gallaudet University
TDI Conference, Albuquerque, NM, October 16-20, 2013

## Slide 2: Overview
Who we are
The state of mobile video calling today
  Interoperability of videophones
  Testing results
Sample of video calls
Battery tests
  Idle 6 hours test
  10 minutes in call test

## Slide 3: Who we are
The Technology Access Program is a deaf-led research center at Gallaudet University
Research areas:
  Telecommunications access
  Videoconferencing access
  9-1-1 access
  Hearing aid compatibility of phones
  And other technology access issues

## Slide 4: Video calling today
Which phone? iPhone or Android i.e. Samsung?
What mobile VRS app do you use for video calls?
  nTouch?
  ZVRS Z5?
  Purple P3?
  Convo?
  CAAGVRS?
  GXPro?

## Slide 5: Video calling today
Do you use VRS or mainstream mobile apps for video calls?
  VRS app on your mobile
  FaceTime
  Skype
  ooVoo
  Tango
  Fring
  Other?

## Slide 6: Video calling today
  It is worth remembering what the purpose of VRS and mobile video calls is: Functional equivalence
  Can deaf and hard of hearing people use telecommunication services in the same unrestricted manner and at the same costs as hearing people?

## Slide 7: Functional Equivalence
Do we have it today?
Do you feel that we have equal access compared to the mainstream?

## Slide 8: Interoperability
Interoperability is a big barrier for us in the video calling world.
  Interoperability: devices from different vendors and providers work with each other.
See what hearing callers can do:

## Slide 9: Voice interoperability
Hearing callers can call each other with landline phones, mobile phones, Internet software, and leave messages via answering machines/voicemail. It just works.

## Slide 10: Interoperability testing
Tested devices, software and apps from 6 VRS providers: CAAG, Convo, Global VRS, Purple, Sorenson, and ZVRS
Also tested three stand alone devices: Purple’s Smart VP, Sorenson nTouch VP and ZVRS’s Z20 to verify if they can receive mobile calls

## Slide 11: Interoperability testing
Last year at the NAD conference, we showed that mobile VRS interoperability was bad.
Has this changed?
We ran tests to find out -

## Slide 12: Testing lab

## Slide 13: Call Test Matrix

## Slide 14: Testing method
Test live call from and to each device/app
Test leaving message on answering machine
  Press “reject call” on answering phone to force answering machine on
  One limitation: Some phones may behave differently if you just let the call ring – but this would have taken too long for all calls

## Slide 15: Testing method
11 x 14 (11 app + 3 VPs) = 308 calls total
All calls use either Wifi or Ethernet. No cellular test calls are used
WiFi tests were done on consumer-grade routers typical of homes for each side of mobile test calls (2 routers)
Each side of call tests uses different Wifi router behind NAT and a different public IP address to simulate real world

## Slide 16: Interoperability Issues
Some highlights:
  Mobile apps have improved since last year
  Live calls work better than leaving messages
Full results on our web site (link is shown on final slide)

## Slide 17: Interoperability Issues
Convo:
  Calling to any Purple videophone resulted in Purple VRS call instead of point to point calls
  Receiving nTouch mobile calls caused black video on Convo side
  Convo app making calls to CAAGVRS app did not ring

## Slide 18: Interoperability Issues
CAAGVRS:
  CAAGVRS iOS app calling to either iOS or Android app of CAAGVRS resulted into black videos
  Convo app calling to CAAGVRS apps did not ring
  No answering machine offered for CAAGVRS customers
  Black video seen on CAAGVRS apps from nTouch app calls

## Slide 19: Interoperability Issues
Global VRS:
  Can not receive calls in our test accounts but can make calls fine
  No answering machine offered for CAAGVRS customers

## Slide 20: Interoperability Issues
Purple:
  Convo calling to any Purple videophone resulted in Purple VRS call instead of point to point calls
  Can't receive nTouch Android calls
  ZVRS callers can't see Purple answering machine greetings

## Slide 21: Interoperability Issues
Sorenson:
  Unable to accept messages on answering machine from non-Sorenson callers
  ZVRS answering machine greeting gets stuck on CONNECTING TO ANSWERING MACHINE graphic
  Receiving mobile calls from nTouch mobile calls caused black video on Convo
  nTouch Android calls can't connect to Purple mobile apps and Purple SmartVP (iOS nTouch worked fine)

## Slide 22: Interoperability Issues
ZVRS:
  Z4 Android to Z20 resulted black video on Z4 side. Was told Z5 Android will solve this soon.
  Black video on ZVRS app/device of Purple answering machine greetings
  nTouch calls leaving answering machine on ZVRS will get stuck on "CONNECTING TO ANSWERING MACHINE" graphic
  Z5 mobile on iPhone/iPad calls get stuck with RINGING or DIALTONE message on completed calls to providers without answering machine

## Slide 23: Types of problems
Videophone does not ring
  … you have no idea that someone called
Black/green screen
  … the caller can’t see you or vice versa
Poor video
  … you can’t do conversation well
Answering machine does not work
  … people can’t leave messages for you

## Slide 24: Statistics
Success rate of making live calls:
Convo: 16 out of 26
CAAG VRS: 24 out of 26
Global VRS: 13 out of 13
Sorenson: 14 out of 26
Purple: 26 out of 26
ZVRS: 25 out of 26
Note: Calling to Global VRS not counted because of test accounts issues

## Slide 25: Statistics
Success rate of receiving live calls:
Convo: 18 out of 22
CAAG VRS: 12 out of 22
Global VRS: 0 out of 11
Sorenson: 33 out of 33
Purple: 23 out of 33
ZVRS: 32 out of 33

## Slide 26: Statistics
Success rate of leaving messages on answering machines:
Convo: 10 out of 26
CAAG VRS: 16 out of 26
Global VRS: 8 out of 13
Sorenson: 9 out of 26
Purple: 16 out of 26
ZVRS: 10 out of 26
Note: Calling to Global VRS not counted because of test accounts issues

## Slide 27: Statistics
Success rate of taking answering machine messages:
Convo: 18 out of 22
CAAG VRS: does not offer answering machine
Global VRS: does not offer answering machine
Sorenson: 6 out of 33
Purple: 18 out of 33
ZVRS: 27 out of 33

## Slide 28: Short Demo
The next slide will have a video playing of selected VRS app calling to either ZVRS’s Z20 or Sorenson’s nVP.
The video will show the quality received from the stand alone VP to the selected VRS app. Not all are the same.
Videos are not sharp as it should be because of a video camera recording off a phone.

## Slide 29: Short demo

## Slide 30: About mobiles
Interoperability among mobiles has improved since last year
  But still is worse than with standalone VPs
Data bandwidth and data caps (2 GB is just 2-4 hours of calling time)
Android support has improved since last year, but still lags months behind iOS
  Fragmentation in cameras, screens, and CPUs
  At least now most popular phones work

## Slide 31: Battery life
Some people think: VRS apps drain your batteries very quickly
That is, you can’t leave them always on.
Is that still true???

## Slide 32: Battery Life
  We ran two battery life tests in this enviroment:
  Strong Wifi signal is used
  Killed all running apps except for selected VRS
  Bluetooth and mobile data were turned off
  Runs on battery only.
  Video call tests used a common looping video on a Mac screen
    Phone cameras were pointed at it
  Two different tests: Idle and in-call.

## Slide 33: Idle Battery Life
  Idle tests (6 hours) for iPhone 5:
  iPhone (No VRS App) 2% drop
  iPhone Z5 1% drop
  iPhone Purple 2% drop
  iPhone CAAG 0% drop
  iPhone Sorenson 0% drop
  All are about the same of using battery while in good Wifi signal. Cellular use on battery may vary.

## Slide 34: Idle Battery Life
  Idle tests (6 hours) for Samsung S3:
  S3 (No VRS App) 11% drop
  S3 Z4 14% drop
  S3 Convo 16% drop
  S3 Purple 20% drop
  S3 CAAG 9% drop
  S3 Sorenson 16% drop
  There were some Android processes we couldn’t control. Cellular use on battery may vary.

## Slide 35: In Call Battery Life
  In Call tests (10 minute) for iPhone 5 & iPad 2:
  iPhone Convo 7% drop
  iPhone Purple 5% drop
  iPhone CAAG 6% drop
  iPhone Sorenson 5% drop
  iPhone Z5 5% drop
  iPhone Facetime 6% drop
  iPad Facetime 0% drop

## Slide 36: In Call Battery Life
  In Call tests (10 minutes) for Samsung S3 & Nexus 7 Tablet:
  S3 Z4 6% drop
  S3 Convo 6% drop
  S3 Purple 5% drop
  S3 CAAG 6% drop
  S3 Sorenson 4% drop
  S3 GoogleTalk 6% drop
  Nexus 7 Tablet GoogleTalk 3% drop

## Slide 37: Battery Life
On iPhones, we saw no difference between leaving the VRS app always on in the background and turning it off.
On Android, VRS apps still eat battery life in the background (but not very much: 6-10% over 6 hours).
We saw no difference between VRS and native apps for battery use during calls
Caution: These were Wifi tests – cellular behavior may be different
Caution: We did not test if the VRS app still was functioning after 6 hours in the background

## Slide 38: Battery life tips
To save battery, it is a good idea to kill all applications that are not needed. Use texting to agree for a video one to one calls. Run VRS app for making calls and for expecting video calls.
Both VRS and native video calls (Facetime, Google Hangouts) drain the battery – 30% per hour – or just 2 to 3 hours of calling time on Wifi.
  Compare to over 10 hours for voice calls
  Is that functionally equivalent?
Fixing battery life during video calls needs to be a priority.

## Slide 39: Acknowledgments
The contents of this presentation were developed with funding from the National Institute on Disability and Rehabilitation Research, U.S. Department of Education, grant number H133E090001 (RERC on Telecommunications Access). However, those contents do not necessarily represent the policy of the Department of Education, and you should not assume endorsement by the Federal Government.

## Slide 40: Questions
Questions? Comments?
Supplemental material:
  http://tap.gallaudet.edu/Conferences/TDI2013/